## Slide 1: WAN Interconnection Technologies and Typical Scenarios of Enterprise Networks

## Slide 2
The WAN provides interconnection services for different users. Because users have various requirements, the WAN provides different interconnection technologies.
WANs can be interconnected through transmission private lines, MPLS private lines, or the Internet. Different interconnection modes require different technologies.
This course compares application scenarios and differences of technologies to help trainees better understand WAN interconnection modes.

## Slide 3
Upon completion of this course, you will be able to:
  Describe the traditional WAN interconnection solution.
  Describe technologies used on WANs.
  Describe three application scenarios of SD-WAN.

## Slide 4
Traditional Interconnection Solution for Enterprise WANs
Application of Enterprise WAN Interconnection Technologies
  Private Line Technologies and Application Scenarios
  VPN Technologies and Application Scenarios
Application Scenarios of SD-WAN

## Slide 5: Typical WAN Interconnection Architecture of an Enterprise Network
There are many WAN interconnection modes for enterprises. Generally, one or more interconnection modes are used based on different enterprise requirements.
Company branch
Private line
(MPLS)
HQ
Company branch
Company branch
Bare optical fiber/SDH/WDM/MSTP
L2TP/SSL VPN
MPLS VPN
PE
PE
P
DSVPN/IPsec VPN
CE
CE
CE
4G/5G
Private line (transmission)
Internet
Company branch

## Slide 6: Comparison Between Private Line and VPN Technologies
Private lines were introduced very early. They can meet interconnection requirements of enterprises and ensure reliability and security. However, private lines are expensive.
With the network development, VPN technologies start to occupy more market shares. However, some industries demanding high security and reliability, such as the financial industry, still want to use private line technologies.
Selecting private line or VPN technologies depend on company's services. The following table compares the two technologies.
Item | Private Line Technology | VPN Technology
Security | Relatively high: depending on ISPs | Very high: Data is encrypted before being transmitted and security control is in the hands of users.
Reliability | High: depending on ISP network reliability | Comparatively high: depending on reliability of Internet lines
Scalability | Medium: depending on ISPs | Based on TCP/IP technology, the access mode is flexible. Scalability is implemented only if the network is reachable.
Investment cost | The private line expense is very high and needs to be paid every month. In addition, the device expense needs to be invested in the initial period of network construction. | One-off device expense is invested, so there is no need to pay monthly operating expenses.
Support for mobile users | Mobile users can only connect to the network connected to a private line, and internal mobile users leaving a LAN cannot access a private network. | Internal mobile users can use the Internet for secure access, eliminating geographical differences.
Transmission bandwidth | Leased bandwidth is low because of the high price. | The Internet is cheap, and the leased bandwidth is high.
Upgrade | Depending on the telecom department | Device upgrade is convenient.

## Slide 7: Introduction to Carriers' Private Lines
Carriers have a large number of line resources and launch different private line services based on different industries and scenarios.
Carriers' high-quality transmission private line services mainly include SDH, MSTP, and bare optical fibers, which are expensive but have excellent performance.
MPLS VPN is another type of private line service provided by carriers. MPLS VPN private lines provide slightly lower performance than transmission private lines but are less expensive.
Carrier's private line (private line network in the financial industry)
Level-1 branch
Level-2 branch
Outlet
Outlet
Level-2 branch
ATM
Outlet
Branch service network
Branch LAN
Branch LAN
The finance industry leases carriers' MSTP/SDH private line services to ensure high network reliability.
MSTP/SDH
MSTP/SDH
Carrier's private line (MPLS VPN network of a provincial library)
County library
County library
County library
Community library
Community library
Community library
Community library
City library
City library
GRE over IPsec (enterprise-built)
MPLS VPN (ISP)
MPLS VPN (ISP)

## Slide 8: Introduction to Enterprise-Built Private Line and VPN
Enterprises can establish VPNs, such as SSL VPN, DSVPN, and IPsec VPN, through carriers' networks.
Some large enterprises have the capability to lay out optical fibers by themselves and can set up enterprise MPLS VPN private lines. However, few enterprises have the capability to lay out optical fibers by themselves.
VPNs built by enterprises are more and more widely used because they are cost-effective, easy to expand, and controllable.
Enterprise-built VPN (VPN of a provincial library)
Enterprise-built private line (MPLS VPN network of the energy industry)
County library
County library
County library
Community library
Community library
Community library
Community library
City library
City library
GRE over IPsec
MPLS VPN (ISP)
MPLS VPN (ISP)
Provincial backbone network
Provincial backbone network
National backbone network
Municipal service network
Municipal service network
Municipal service network
Municipal service network
MPLS VPN (self-built)
MPLS VPN (self-built)

## Slide 9
Traditional Interconnection Solution for Enterprise WANs
Application of Enterprise WAN Interconnection Technologies
  Private Line Technologies and Application Scenarios
  VPN Technologies and Application Scenarios
Application Scenarios of SD-WAN

## Slide 10: Overview of Private Line Technologies
Private line technologies were introduced very early. With the development of networks, many technologies, such as frame relay (FR) and ATM, are no longer used. Currently, the following private line technologies are widely used:
  Bare optical fiber: Carriers provide bare optical fibers along which no intermediate device is deployed. Therefore, bare optical fibers are expensive.
  SDH/MSTP/WDM: Transmission private lines use transmission devices to build hard pipes on optical fibers, ensuring good performance. The price of such private lines is lower than that of bare optical fibers.
  MPLS VPN: MPLS private lines use Ethernet for access and do not have hard pipes. The performance of MPLS VPN is poorer than that of transmission private lines, but the price of MPLS VPN is the cheapest among all private lines.

## Slide 11: Introduction to Bare Optical Fibers
A carrier provides a bare optical fiber line where no intermediate device is deployed. The network capacity depends on the enterprise devices at both ends of the bare optical fiber.
Bare optical fibers are charged based on the distance. A longer distance indicates a higher cost. Generally, the maximum distance of a hop of an optical fiber is 300 km. If the distance between two sites exceeds 300 km, a repeater needs to be installed.
Enterprise branch
HQ
Carrier
Optical network
Enterprise transmission device
Enterprise transmission device

## Slide 12: Application Scenario of Bare Optical Fibers
Application scenario of bare optical fibers
Bare fibers can be leased between the main campus and branch campus in the same city to connect the two campuses, simplifying network management and access authentication management.
ISP1
ISP2
Lease carrier's bare optical fiber
Main campus
Branch campus

## Slide 13: Introduction to SDH/MSTP/WDM Private Lines
Enterprises that require long-distance transmission and high network reliability and security can lease SDH/MSTP/WDM private lines.
This type of private line is a transmission private line. Tenants exclusively occupy part of the bandwidth of the transmission private line. Because multiple users share the transmission private line, its price is lower than that of bare optical fibers. Although transmission private lines are shared by tenants, they exclusively occupy bandwidth and use hard pipes. Therefore, they deliver high reliability and security.
MSTP and WDM private lines are widely used on the live network, and SDH private lines are still used in a few areas.
Enterprise branch
HQ
Carrier
Transport network
SDH/MSTP/WDM device
SDH/MSTP/WDM device
Notes: SDH is a TDM system and a traditional circuit scheduling mode.
The multi-service transport platform (MSTP) receives, processes, and transmits TDM, ATM, and Ethernet services.
WDM uses multiple lasers to transmit multiple beams of lasers with different wavelengths on a single optical fiber. The transmission bandwidth of WDM devices is high, and the bandwidth on the live network can reach 8 Tbit/s.

## Slide 14: Application Scenarios of SDH/MSTP/WDM Private Lines
Application scenarios of SDH/MSTP/WDM private lines
To ensure high reliability and security, MSTP or SDH private lines are used for interconnection between financial branches.
MSTP/SDH
MSTP/SDH
MSTP/SDH
HQ
Branch
Branch
Outlet
Outlet

## Slide 15: MPLS VPN Private Line
Backbone
MPLS VPN technology is widely used in enterprise interconnection scenarios. MPLS L2VPN or MPLS L3VPN can be deployed based on enterprise requirements. MPLS VPN makes a compromise between the cost and performance, so it is very popular.
For enterprises that can build their own WANs, such as railways and electric power companies, MPLS VPN is an easy-to-manage and low-cost VPN technology. For enterprises that cannot build their own WANs, MPLS VPN is expensive.
The enterprises that have security requirements can use MPLS VPN line as the primary link and GRE over IPsec line as the backup link.
Branch
MPLS VPN
PE
PE
P
CE
HQ
CE

## Slide 16: Application Scenario of MPLS VPN
Application scenario of MPLS VPN
The MPLS L3VPN solution is widely used on the live network. Some large-scale networks may use inter-AS MPLS L3VPN.
Provincial backbone network
Provincial backbone network
PE
PE
PE
PE
ASBR
ASBR
ASBR
ASBR
ASBR
ASBR
ASBR
ASBR
Enterprise A
Enterprise B
Enterprise A
Enterprise B
RR
RR
RR
RR
RR
RR
Core backbone network
VPNv4 peer
MPLS L3VPN traffic
Notes: There are three types of inter-AS MPLS L3VPN solutions: Option A, Option B, and Option C.
Option A applies to small-scale inter-AS MPLS L3VPNs. Option B applies to medium- and large-scale inter-AS MPLS L3VPNs. Option C applies to large-scale or super-large-scale inter-AS MPLS L3VPNs.

## Slide 17
Traditional Interconnection Solution for Enterprise WANs
Application of Enterprise WAN Interconnection Technologies
  Private Line Technologies and Application Scenarios
  VPN Technologies and Application Scenarios
Application Scenarios of SD-WAN

## Slide 18: Overview of VPN Technologies
VPN technologies are widely used in scenarios where enterprises build their own Internet.
VPN technologies can be classified into the following three types based on the usage:
  Access VPN (virtual private network for remote access): also called dial-up VPN or VPDN. Generally, L2TP VPN technology is used.
  Intranet VPN (internal virtual private network of an enterprise): connects gateways and connects resources of the same company through the company's network architecture. Generally, GRE or DSVPN technology is used.
  Extranet VPN (extended internal virtual private network of an enterprise): is used to build an extranet with the enterprise network of a partner. Generally, SSL VPN technology is used.
Notes: By service usage:
  Access VPN: enables mobile employees, remote office employees, and remote small-sized offices to establish private network connections with enterprise intranet and extranet through the public network. There are two types of access VPN connections: client-initiated and NAS-initiated VPN connections.
  Intranet VPN: Intranet VPN is an extension or replacement of traditional private lines or other enterprise networks to connect distribution points within an enterprise through a public network.
  Extranet VPN: extends enterprise networks to suppliers, partners, and even clients over the public network.
According to layers of tunnels in the OSI model:
  Layer 2 tunneling protocol: encapsulates PPP frames into a tunnel. Layer 2 tunneling protocols include the Point-to-Point Tunneling Protocol (PPTP), Layer 2 Forwarding (L2F), and Layer 2 Tunneling Protocol (L2TP).
  Layer 3 tunneling protocol: Only Layer 3 packets are carried in a tunnel. Existing Layer 3 tunneling protocols include Generic Routing Encapsulation (GRE) and IPsec. IPsec includes the Authentication Header (AH) protocol and Encapsulating Security Payload (ESP) protocol.

## Slide 19: Access VPN Overview
Access VPN uses VPDN technology. VPDN is a type of VPN service based on dial-ups. It can be used for enterprise interconnection or remote access to enterprise networks.
VPDN tunnel
VPDN tunnel
VPDN
PC
PC
PC
PC
Enterprise branch
HQ
Dialing user
Dial-up network
NAS
(LAC)
LNS
RADIUS server
RADIUS server
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: VPDN is implemented by using a tunneling technology. That is, data of an enterprise network is encapsulated in a tunnel for transmission. On an interface between the source LAN and public network, the tunneling technology encapsulates data as a payload in a data format that can be transmitted on a public network. On an interface between the destination LAN and the public network, it decapsulates data to extract the payload. The logical path through which encapsulated data packets are transmitted on the Internet is called a tunnel. To ensure that data is encapsulated, transmitted, and decapsulated smoothly, the communication protocol is the core.
VPDN provides three common tunneling technologies:
  Point-to-Point Tunneling Protocol (PPTP)
  Layer 2 Forwarding (L2F)
  Layer 2 Tunneling Protocol (L2TP)

## Slide 20: PPTP Overview
PPTP is the first VPN protocol and has been developed for more than 20 years. This protocol relies on encryption, authentication, and PPP for negotiation. It requires only the user name, password, and server address for connection setup.
PPTP is fast, but has weak encryption. Among all VPN protocols, PPTP has the lowest encryption level and must be based on IP networks.
PC
PC
PPTP
Client
PPTP
Client
PPTP tunnel
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 21: L2F Overview
After PPTP was released, Cisco developed L2F to try to fix defects of PPTP.
L2F encapsulates packets of link-layer protocols (such as HDLC, PPP, and ASYNC) for transmission. Therefore, the link layer of a network is independent of link-layer protocols of users.
L2F is a secure communication tunneling protocol, but it does not provide the standard encryption method. Therefore, it has become an outdated tunneling protocol.
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 22: L2TP Overview
WAN
L2TP, an open standard of IETF, combines advantages of PPTP and L2F. L2TP is especially suitable for setting up a VPN in remote access mode and has become a de facto industry standard.
L2TP is only a tunneling protocol and does not provide encryption. Therefore, L2TP is usually used together with IPsec.
L2TP is one of commonly used enterprise interconnection technologies. When L2TP is used, the AAA server is required. L2TP is a good choice for constructing an L2VPN.
LNS
L2TP client
(LAC)
Enterprise branch
HQ
L2TP Tunnel
L2TP Tunnel
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 23: Application of Access VPN on the Live Network
Access VPN is mainly used for remote access of intranet users, and L2TP over IPsec is most widely used.
PPTP requires the support of the Windows operating system. In addition, the IP address of the Windows server on the intranet needs to be mapped through NAT for extranet access. Therefore, PPTP is difficult to deploy and is seldom used.
Application of L2TP over IPsec on the live network
L2TP connections can also be used between branch sites. However, L2TP cannot transmit multicast data between the headquarters and branches. Therefore, L2TP is mainly used for remote user access on the live network.
HQ
Internet
LNS
Traveling employee
Traveling employee
L2TP Over IPsec
L2TP Over IPsec
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 24: Intranet VPN Overview
Internet
Intranet VPN technology is used to construct a VPN between gateways based on the Internet. The main technologies used are GRE and DSVPN.
GRE and DSVPN technologies are used to establish a VPs between enterprise branches and the headquarters.
PC
PC
PC
PC
Enterprise branch
HQ
PC
PC
Enterprise branch
GRE, DSVPN
GRE, DSVPN
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: Intranet VPN uses the following technologies:
  GRE
  GRE over IPsec
  DSVPN
  DSVPN IPsec

## Slide 25: GRE Overview
GRE is used to encapsulate packets of some network layer protocols (such as IP, IPX, and AppleTalk) so that the encapsulated packets can be transmitted over the network on which another network layer protocol is applied.
GRE is typically used on networks with a few branch sites.
Link layer
GRE
IP
IP
Payload
Flags
Protocol Type
Internet
PC
PC
PC
PC
Enterprise branch
HQ
GRE tunnel
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: GRE is a Layer 3 tunneling technology. A GRE tunnel is a virtual P2P connection that transmits encapsulated data packets.
The two ends of the GRE tunnel are tunnel interfaces which encapsulate and decapsulate data packets. The tunnel interface that sends encapsulated packets is called the tunnel source interface, and the one that receives these packets on the peer end is called the tunnel destination interface.
The packet encapsulation process in the figure is as follows:
  After receiving an IP packet, Router_A's interface that connects to the enterprise branch sends a packet to the IP protocol module.
  The IP protocol module checks the destination address in the packet header to determine how to forward this packet. If the packet is destined for the other end of the GRE tunnel, the IP protocol module sends the packet to the tunnel interface.
  After receiving the packet, the tunnel interface encapsulates the packet using GRE and delivers the packet to the IP protocol module.
  The IP protocol module encapsulates the GRE packet using a new IP packet header. The source address is the address of the tunnel source interface, and the destination address is the address of the tunnel destination interface. Then the IP protocol module forwards the encapsulated IP packet from the WAN interface (tunnel source interface) based on the destination address and routing table.

## Slide 26
Notes: As the reverse of encapsulation, the decapsulation process is as follows:
  Router_B receives an IP packet from its physical interface connected to the Internet and checks the destination address. If the destination is Router_B and the protocol ID in the IP packet header is 47 (indicating GRE packet), Router_B removes the IP packet header and sends the packet to the GRE module.
  The GRE module verifies the checksum and key fields, removes the GRE header, and sends the packet to the IP module.
  The IP protocol module forwards the packet to the enterprise headquarters.

## Slide 27: Overview of GRE over IPsec
GRE does not support encryption. IPsec supports only the IP protocol and does not support multicast.
GRE over IPsec combines advantages of both GRE and IPsec, and offsets their disadvantages.
GRE over IPsec is a point-to-point VPN technology commonly used by enterprises.
PC
PC
PC
PC
IPsec tunnel
IPsec tunnel
GRE tunnel
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: GRE encapsulates multicast data to allow data to be transmitted through GRE tunnels. Currently, IPsec can encrypt only unicast data. If multicast data, such as routing protocol, voice, and video data, needs to be transmitted over IPsec tunnels, a GRE tunnel can be established to encapsulate multicast data, and then IPsec encrypts the encapsulated packets. In this way, multicast data is encrypted and transmitted in the IPsec tunnel.
GRE over IPsec combines advantages of both GRE and IPsec. It enables a network to support multiple upper-layer protocols and multicast packets, as well as packet encryption, identity authentication, and data integrity check.
GRE over IPsec encapsulates packets using GRE, and then IPsec.
GRE over IPsec supports the following encapsulation modes:
  Tunnel mode
  Transport mode

## Slide 28: DSVPN Overview
DSVPN overcomes defects of GRE over IPsec and enables enterprises with a large number of branches to easily build VPN networks.
DSVPN is a technology that dynamically establishes GRE tunnels. It uses the Next Hop Resolution Protocol (NHRP) to dynamically collect, maintain, and advertise information such as the public IP address of each spoke, allowing the source branch to obtain the public IP address of the destination branch.
DSVPN uses mGRE technology to enable VPN tunnels to transmit multicast and broadcast packets, and a tunnel interface can establish VPN tunnels with multiple peers.
The GRE tunnel established by DSVPN can still use IPsec technology to ensure tunnel security.
Internet
Hub
Spoke
Spoke
Spoke
Dynamic mGRE tunnel
Data between spokes
Static mGRE tunnel
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: DSVPN resolves the following defects of GRE over IPsec:
  All traffic must pass through the hub.
  The hub configuration needs to be modified when a site is added.
  If spokes use dynamic addresses, problems may occur when P2P GRE is deployed.

## Slide 29: Application of Intranet VPN on the Live Network
On the live network, intranet VPN is mainly used for interconnection between enterprise branches and the headquarters and between branches.
GRE over IPsec is widely used on the live network. For enterprises with many branches, Efficient VPN can be used to simplify the branch configuration. IPsec link redundancy can be deployed to ensure GRE reliability.
Application of GRE over IPsec
DSVPN is seldom used on the live network due to the following reasons: 1. Many enterprises expect that traffic between branches can pass through the headquarters to facilitate management. 2. Enterprise O&M personnel just have a basic understanding of DSVPN, which is inconvenient for O&M.
HQ
Internet
Branch
Branch
GRE over IPsec
GRE over IPsec
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 30: Extranet VPN Overview
Internet
Extranet VPN is mainly used to build secure access services between customers or suppliers. Traveling employees can also use extranet VPN to access the enterprise network.
Extranet VPN mainly uses SSL VPN and L2TP.
PC
PC
PC
PC
Customer
HQ
SSL VPN/L2TP
SSL VPN/L2TP
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: Extranet VPN mainly uses the following technologies:
  SSL VPN
  L2TP VPN

## Slide 31: SSL VPN Overview
Internet
SSL VPN is mainly used by traveling employees to remotely access the enterprise intranet, which is an extension of the enterprise intranet on the WAN.
SSL VPN authenticates and controls users based on HTTP. Users do not need to configure SSL VPN, which is easy to use.
SSL VPN tunnel
SSL VPN client
SSL VPN gateway
Web page proxy
File sharing
Port forwarding
Network extension
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: SSL VPN is a VPN remote access technology based on SSL. Mobile users (referred to as remote users in SSL VPN) can use SSL VPN to securely and conveniently access enterprise intranets and intranet resources, improving work efficiency.
Before SSL VPN is developed, VPN technologies such as IPsec and L2TP are used to enable remote user access. However, these VPN technologies have the following disadvantages:
  Remote users need to install specific client software on their terminals, leading to difficult network deployment and maintenance.
  The IPsec or L2TP VPN configuration is complex.
  Network management personnel cannot perform fine-grained control over the permissions on enterprise intranet resource access by remote users.

## Slide 32: Application of Extranet VPN
It is convenient for external users to access the intranet through SSL VPN. They can directly access the intranet after passing web page authentication, without installing a client. In addition, there are many SSL VPN service options, such as web page proxy, file sharing, port forwarding, and network extension.
Application of SSL VPN
SSL VPN is easy to use. You can use a browser to access the intranet. However, not all routers support SSL VPN. For routers that do not support SSL VPN, you can use L2TP to establish connections with the intranet.
Remote office
Partner
Mobile user
Port 443
Internet
HQ
Web page server
OA
Email server
ERP
FTP server
NMS
Branch user
Partner
Network extension
Web page proxy
File sharing
Port forwarding
SSL VPN gateway
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 33
Traditional Interconnection Solution for Enterprise WANs
Application of Enterprise WAN Interconnection Technologies
  Private Line Technologies and Application Scenarios
  VPN Technologies and Application Scenarios
Application Scenarios of SD-WAN

## Slide 34: SD-WAN Technology Review
Service- and intent-orientation, implementing network orchestration and automatic provisioning.
Traditional network service provisioning requires professional network engineers to perform planning, configuration, and O&M, and then run commands or use the NMS software to configure devices one by one based on the planned services.
Traditional network
The SDN network uses a centralized network control system to abstract, orchestrate, and automatically provision network services on demand. It shields technical implementation details of the network and opens only service-oriented interfaces and parameters to users.
SDN
SD-WAN controller
Branch site
Branch site
HQ
Branch site
Enterprise WAN interconnection
Provision services
IP overlay tunnel
IP overlay tunnel
IP overlay tunnel
Enterprise
Propose requirements

## Slide 35: Enterprise-built SD-WAN Scenario
Legacy site
Enterprise HQ/DC
Enterprise branch
SD-WAN controller
  The SD-WAN controller is deployed on the WAN to centrally manage CPEs and implement ZTP. This shortens the service provisioning time, and helps enterprises cope with challenges brought by cloud services and implement service change on demand.
  Large enterprises with a large number of branches, such as financial institutions, retail chains, and gas stations, can deploy their own SD-WAN controller at the headquarters to set up their own SD-WAN networks and manage their SD-WAN services.
RR
CPE
CPE
SD-WAN gateway
Cloud
CPE
Device Model | Function
SD-WAN controller | Is the core of the SD-WAN solution. It uniformly manages CPEs, automatically delivers services, and implements unified control of overlay networks.
RR | Is a distributed control component, which distributes VPN routes between CPEs based on VPN topology policies.
CPE | Is an egress device of an enterprise branch, the headquarters, and a DC.
SD-WAN gateway | Is an intermediate gateway that connects an SD-WAN network to a non-SD-WAN network.
Internet
MPLS
LTE

## Slide 36: MSP-built SD-WAN Scenario
Enterprise HQ/DC
Enterprise branch
SD-WAN controller
  The management service provider (MSP) provides a unified SD-WAN controller to provide SD-WAN services for multiple enterprises. The MSP builds its own PoP backbone network and provides PoP access. Enterprises can access the nearest PoP, implementing high-quality enterprise interconnection. The PoP supports multiple tenants and provides access for multiple enterprises.
  Enterprises can serve as tenants to lease SD-WAN services provided by MSPs. An enterprise tenant can manage the SD-WAN services of all sites belonging to it. However, it cannot view the SD-WAN services of other tenants.
RR
CPE
CPE
MSP multi-POP backbone network
PoP
PoP
LTE
Internet
MPLS
LTE
Internet
MPLS

## Slide 37: Carrier-built SD-WAN Scenario
  Carriers provide SD-WAN services for multiple enterprises through the SD-WAN controller.
  Enterprises can serve as tenants to lease SD-WAN services provided by carriers. An enterprise tenant can manage the SD-WAN services of all sites belonging to it. However, it cannot view the SD-WAN services of other tenants. Enterprises either manage and control their SD-WAN services based on the tenant permissions assigned by carriers, or they entrust their SD-WAN services to carriers for management and control.
  SD-WAN gateways implement flexible interconnection and fast compatibility between the SD-WAN network and traditional carrier's backbone network.
Carrier DC
Retail enterprise
HQ/DC
Technology enterprise
HQ/DC
Enterprise network
Carrier network
Carrier's management center
RR
RR
SD-WAN gateway
SD-WAN gateway
SD-WAN gateway
CPE
CPE
CPE
CPE
CPE
CPE
SD-WAN controller
Carrier's backbone network
LTE
Internet
Internet
MPLS

## Slide 38
(Multiple-answer question) Which of the following are private line technologies?
  MPLS VPN
  SDH
  IPsec VPN
  L2TP
Notes: 1. AB

## Slide 39
Enterprise WANs can be connected to private lines or VPNs.
  Private lines include bare fibers, transmission private lines (SDH and MSTP), and MPLS private lines (MPLS L2/L3 VPN).
  VPNs include GRE, GRE over IPsec, L2TP VPN, and SSL VPN.
The SD-WAN solution can build enterprise WANs based on private lines or VPNs.
SD-WAN technology application scenarios are as follows:
  Enterprise-built SD-WAN scenario
  MSP SD-WAN Scenario
  Carrier SD-WAN Scenario